## Slide 1
Unified
Character
Recognition
Sneha Gandewar
Neha Jain
Amey Patil

## Slide 2: Overview
Introduction to various pattern recognition systems
Plan for implementation
Experiments and Results

## Slide 3: Printed Character Recognition
PCR engines turn images of machine-printed characters into machine-readable characters
Images of machine-printed characters are extracted from a bitmap

## Slide 4: Intelligent Character Recognition
ICR reads images of hand-written character and converts them into machine-readable characters
Recognition of numeric characters is much more accurate than the recognition of letters

## Slide 5: Optical Mark Recognition
OMR technology detects the existence of a mark, not its shape
OMR forms usually contain small ovals, referred to as 'bubbles’, that the respondent fills in
OMR cannot recognize alphabetic or numeric characters

## Slide 6: Magnetic Ink Character Recognition
MICR is a specialized character recognition technology to facilitate cheque processing
Since background designs can interfere with optical recognition, magnetic ink is used

## Slide 7: Magnetic Ink Character Recognition

## Slide 8: Barcode Recognition
A barcode is a machine-readable representation of information
They can be read by optical scanners
1D Barcode

## Slide 9: Plan for Implementation
Pre-Processing
Segmentation
Feature Extraction
Neural Classification

## Slide 10
Pre-Processing
Binarization
Pre-Thinning
Thinning
Post-Thinning

## Slide 11
Binarization
Coloured images to two colours, black and white
Single bit per pixel
Greatly reduces the complexity of the image
Algorithms
Thresholding
Local Binarization

## Slide 12
Pre-Thinning
Reduces the noise due to the binarization
P3 | P2 | P1
P4 | P | P0
P5 | P6 | P7
B(P) = P0 + P2 + P4 + P6
If B(P) < 2 then
set P' to black
Else If B(P) > 2 then
set P' to white
Else
set P' to the value of P

## Slide 13
Thinning
Technique that transforms bold thick letters to thin letters of one pixel width
Original Character Image Thinned Character Image

## Slide 14
Why thinning is required?
Reduces the amount of information to be processed
Shape analysis is easy
Eliminates some of the contour distortions
Retains significant features of the patterns

## Slide 15
Post-Thinning
To correct the deformation of the image
Deformation is caused due to discontinuity
Gaps creates pseudo endpoints
From the end points, paths are explored in all directions looking for the nearest black pixel
Threshold distance

## Slide 16
Post-Thinning
Example of an original character and its thinned image
after applying the post-thinning algorithm

## Slide 17
Segmentation
Method to isolate characters
Enhances character recognition efficiency
Projection analysis
Detection of white space between successive letters
Basis for the segmentation in non-cursive writing

## Slide 18
Segmentation
Character
Character
C | h | a | r | a | c | t | e | r

## Slide 19
Feature Extraction
Transforming the input data into the set of features
The process determines various attributes or properties associated with a region
Group of pixels
Normalization

## Slide 20
Feature Extraction
000000000000000000000000000000
000000000000001100000000000000
000000000000011110000000000000
000000000000111111000000000000
000000000001111111100000000000
000000000011100001110000000000
000000000111000000111000000000
000000001110000000011100000000
000000011111111111111110000000
000000011111111111111111000000
000000111000000000000011100000
000001110000000000000001110000
000011100000000000000000111000
000111000000000000000000011100
001110000000000000000000001110
A

## Slide 21
Feature Extraction
000000000000000000000000000000
000000000000001100000000000000
000000000000011110000000000000
000000000000111111000000000000
000000000001111111100000000000
000000000011100001110000000000
000000000111000000111000000000
000000001110000000011100000000
000000011111111111111110000000
000000011111111111111111000000
000000111000000000000011100000
000001110000000000000001110000
000011100000000000000000111000
000111000000000000000000011100
001110000000000000000000001110

## Slide 22
Feature Extraction

## Slide 23: Classification
Neural Network
Training
Learning
Application
Error Back-Propagation algorithm

## Slide 24: Classification

## Slide 25
Experimentation
Experiment has been carried out on a sample OMR specification
A skew angle of ±5° on the input OMR sheet is acceptable
The output text file will have question numbers and corresponding answers marked in the answer-sheet

## Slide 26
Steps undertaken
Reading the OMR sheet
Thresholding
Morphological functions
  Dilation
  Majority
Comparing the text file with actual solution for efficiency

## Slide 27
Converting the input image to grayscale image
graythresh(I) computes a global threshold (level)
level converts an intensity image to a binary image
level is a normalized intensity value that lies in the range [0,1]
Thresholding

## Slide 28
Original image
Image after
thresholding

## Slide 29
Broad set of image processing operations that process images based on shapes
The operations apply a structuring element to an input image, creating an output image of the same size
The value of each pixel in the output image is based on a comparison of the corresponding pixel in the input image with its neighbors
Morphological Functions

## Slide 30
DILATION
Adds pixels to the boundaries of objects in an image
Number of pixels depend on the size and shape of the structuring element(set of co-ordinates) used to process the image
Dilation of foreground pixels is equal to erosion of background pixels

## Slide 31
Thresholded image
Dilated image

## Slide 32
MAJORITY
Considers a 3-by-3 neighbourhood matrix
Sets a pixel to 1 if five or more pixels among the eight neighbours are 1's; otherwise, it sets the pixel to 0

## Slide 33
Centres of the filled circles(marked answers) are found
Duplicate centers are eliminated, if any

## Slide 34
Using the corresponding co-ordinates, each bubble is mapped to its correct question and option number

## Slide 35
To implement all the proposed recognition systems
To train the network with diverse training samples
To improve the system so as to recognize number of symbols and characters
All the ground work has been laid in preparation for the implementation of the UCR
Future planning

## Slide 36
Thank You